## Slide 1
CONTROL SYSTEMS COURSE PROJECT
PID Thermal Control for Heavy-Duty Trucks
Holding engine coolant at 90 °C with a SIMC-tuned PID controller driving the radiator fan, modelled and simulated in MATLAB

## Slide 2
Problem Definition & System Inefficiencies
Mechanical Cooling
Today's wax thermostat, on/off fan clutch and belt-driven pump do not follow cooling demand: the thermostat acts like a P-only controller and leaves a temperature offset.
Thermal Inertia
The engine block, coolant and oil store about 720 kJ/K, so the coolant reacts slowly (≈ 851 s) and a load increase can push it past 105 °C within minutes.
Control Objective
▪
Hold the coolant at 90 °C when the engine load rises.
▪
Stay well below the 105 °C limit with zero steady-state offset.
▪
Build the model only from published engine, radiator and material data.

## Slide 3
Control Architecture
Plant Model
Linearised at 90 °C, 30 % load
Controller: PID
Tuning: SIMC rule (Skogestad)
•
Fan path: G(s) = 38.1 / ((851s + 1)(11.3s + 1)).
•
Load path: Gd(s) = 2.0 / (851s + 1).
•
Built from Volvo D13 data, a truck/bus radiator study and property tables.
•
One feedback loop on coolant temperature, set-point 90 °C.
•
Drives the radiator fan air flow, 0–4.5 kg/s.
•
Gains from the SIMC rule: Kp = 2.48, Ki = 0.044, Kd = 22.4.

## Slide 4
Variable Mapping
Controlled Variable (y)
Manipulated Variable (u)
Disturbance (d)
Coolant temperature T_c
Set-point: 90 °C
Limit: 105 °C
Radiator fan air flow
Range: 0–4.5 kg/s
Pump fixed at 3.25 kg/s
Engine load (%)
Test: 30 → 70 % over 60 s
Ambient air at 30 °C

## Slide 5
Thermal Plant Model
The coolant temperature follows the energy balance of the lumped engine mass, linearised at 90 °C and 30 % load:
Model Simplifications:
•
Engine block, coolant and oil are lumped as one mass, C = 720 kJ/K; the coolant loop adds an 11.3 s lag.
•
Fan heat removal ε·ṁ_f·c_p·(T − T_air) is linearised around the operating fan flow of 1.58 kg/s.

## Slide 6
Metric | Outcome
Peak temperature | No PID: 159.8 °C after 30 min; PID: 90.60 °C
Passes 105 °C | No PID: after about 4 min; PID: never
Steady-state offset | No PID: 69.8 K; PID: 0
Settling (±0.1 K) | PID: 159 s; fan peaks at 3.96 kg/s
Implementation Methodology & Validation
Project Execution Phases
Simulation Results
1.
Build the lumped energy-balance model from published data.
2.
Linearise it into fan-path and load-path transfer functions.
3.
Tune the PID with the SIMC rule; check stability with pole().
4.
Simulate the load rising 30 → 70 % with lsim() in MATLAB.
5.
Compare the coolant temperature with and without the PID.

## Slide 7
Trade-off Analysis: Conventional Cooling vs. PID Control
Mechanical Thermostat and Fan Clutch vs. Electric Fan with PID
The Conventional Approach (Mechanical)
The Control Approach (PID + Electric Fan)
•
No extra hardware; fully mechanical.
•
Thermostat acts like P-only control and leaves an offset.
•
On/off fan clutch makes the temperature swing.
•
Software-defined control of an electric radiator fan.
•
Zero steady-state offset; only 0.6 K peak rise in our test.
•
Needs a temperature sensor and electric actuators.

## Slide 8
Conclusion
A PID controller with SIMC-tuned gains, driving the radiator fan, holds the truck engine coolant at 90 °C: when the load rises from 30 to 70 %, the temperature peaks at only 90.60 °C, while without control it passes 105 °C within about 4 minutes.